## Slide 1: Towards an explicit RTM stencil computation framework on KALRAY TURBOCARD2
Yann Kalemkarian | yann.kalemkarian@kalrayinc.com
Benoît Ganne | benoit.ganne@kalrayinc.com
Chris Piercy | christopher.piercy@kalrayinc.com

## Slide 2: What are we doing at Kalray
We design processors, and produce them :
  It is called MPPA
We design some boards :
  One with 4 MPPA, looks like an accelerator
We have a software ecosystem :
  Compile, link with optimized libraries, debug with cycle accurate tools

## Slide 3: Kalray at a glance
Fabless semiconductor company founded in 2008
Industry-recognized R&D teams, with unique experience in developing leading-edge many-core technologies (HW, SW and overall system)
Holds significant patents (50+) and continues to extend its portfolio
US, Japan & France

## Slide 4: Real Time SuperComputing on a Chip
Kalray recognized critical industry needs
  how to provide more processing performance without increasing power consumption
  how to integrate more and more applications and functions into a single chip
  while guaranteeing the response time (latency)
The industry has reached physical limits
since 2005 due to thermal dissipation
Parallel processing approaches become
necessary:
  Multi-cores architectures: standard CPU duplicated
  Many Cores: optimized CPUs in performance/size and power duplicated n times

## Slide 5: Kalray created: Real Time Supercomputing on a Chip
Real Time CLOUD COMPUTING
  Video Broadcast
  Software Defined Network
  Network Function Virtualization
  Software Defined Storage
INTENSIVE COMPUTING
Oil and Gas
Finance / HFT
Crypto / Defense
Numerical Simulation
Life sciences
to address the following Markets:
EMBEDDED SYSTEMS
  Transport
  Aerospace/Defence
  Industrial Automation

## Slide 6: KALRAY TURBOCARD2 scalable accelerator key facts
PCIe Gen3 16x
IEEE-754 SP/DP FPU
8 DDR3 channels
  Up to 32GB DDR SODIMM
  Up to 100GB/s
1024+ cores, 128MB on-chip memory
Scalable
  Direct multi-boards interconnects
  Low latency
Standard tools
  C, C++, FORTRAN, OpenMP
  GCC-4.9 and GDB-7.3
  OpenCL
Notes: Read +

## Slide 7: KALRAY TURBOCARD Roadmap
TURBOCARD2: available now
  4 x MPPA-256 ANDEY @400MHz
  1 TFLOPS SP / 300 GFLOPS DP
  32GB DDR3 1600 MT/s, 8-channels
Up to 4 TFLOPS SP / RU (eg. HP SL270)
Up to 1.2 TFLOPS DP / RU (eg. HP SL270)
TURBOCARD3: available 4Q ‘15
  4 x MPPA-256 BOSTAN @800MHz
  3.2 TFLOPS SP / 1.6 TFLOPS DP
  64 bits architecture
  64GB DDR3 2133 MT/s, 8-channels
Up to 13 TFLOPS SP / RU
Up to 6.4 TFLOPS DP / RU
Software 100% compatible w/ TURBOCARD2

## Slide 8: KALRAY TURBOCARD2 scalable accelerator Details
1024 Kalray programmable cores
Manycore Processor
Compute Cluster
VLIW Core
TURBOCARD2
  5-issue VLIW architecture
  Predictability & energy efficiency
  32-bit/64-bit IEEE 754 FPU
  MMU for rich OS support
  16 PE cores + 1 RM core
  NoC Tx and Rx interfaces
  Debug Support Unit (DSU)
  2 MB of shared memory
  16 compute clusters
  4 I/O subsystems with quad-core SMP and DDR memory access
  2 Networks-on-Chip
  4 MPPA-256 processors
  8 DDR3 SODIM
  PCIe Gen3 16x to host
  NoCX between MPPA

## Slide 9: KALRAY TURBOCARD2 S/W stack
POSIX threads + OpenMP
Kalray Exokernel
GNU C, C++, Fortran
MPPA® platforms
libNoC
OpenCL runtime
OpenCL
Legend
Communication
Languages
Runtime
Librairies
Distributed Shared Memory
RTEMS - LINUX
OS
Domain Specific Languages and Librairies

## Slide 10: Compiler, Debuggers & System Trace
Compiler
  gcc version 4.9
  C89, C99, C++ and Fortran
  GNU Binary utilities 2011 (assembler, linker, objdump, objcopy, etc.)
  Standard C libraries: uClibc, Newlib +
  Linear Assembly Optimizer (LAO) for VLIW Optimizations
Debuggers
  GDB version 7.3
  Each core seen as a thread
  Watchpoint / breakpoint/ …
System trace
  Linux Trace Toolkit NG based
    low latency
    on demand activation
  Eclipse-based system trace viewer
  Deep insight of execution at system level

## Slide 11: MPPA trace viewer

## Slide 12: Port the Science, not the code!
Standard OpenMP programming model
  GCC / GFORTRAN / G++
Dedicated libraries for specific domains
  HEVC
    x265/FFMPEG seamless integration
  Cryptography
    OpenSSL support
  Financials Monte Carlo
    State-of-the-art optimized RNG libraries
  Oil & Gas seismic migration
    Optimized stencils libraries

## Slide 13: KALRAY TURBOCARD2, serving the Next Generation Oil and Gas
Optimized core
Massively Parallel: 1024 compute cores
No branching / SIMD penalty
IEEE-754 SP/DP FPU
High density
  High computation capability with low power consumption Turbocard2:
    1TFlops for Turbocard2
    100W
  32GB of 8-channels DDR3 on board
Performance Scalability
  Linear scaling with number of cores
  Network on chip extension (NoCX) for Multi-TURBOCARD2 systems
Software reuse
  Reuse existing seismic kernels
  C/C++/Fortran
    GCC/GFORTRAN 4.9
  OpenMP-3
  Full-flavored debug environment
    GDB
  Flexible trace system

## Slide 14: Study : Seismic processing on MPPA (single chip)
Marcio Castro, Fabrice Dupros, Emilio Francesquini, Jean-François Méhaut, and Philippe O. A. Navaux: Energy Efficient Seismic Wave Propagation Simulation on a Low-power Manycore Processor, Europar14 (Aug 2014), Portugal

## Slide 15: Study : Seismic processing on MPPA (single chip)
Marcio Castro, Fabrice Dupros, Emilio Francesquini, Jean-François Méhaut, and Philippe O. A. Navaux: Energy Efficient Seismic Wave Propagation Simulation on a Low-power Manycore Processor, Europar14 (Aug 2014), Portugal
Notes: Used « prefetching scheme »

## Slide 16: Seismic processing on TURBOCARD2
Stencil computation is mostly IO-bound
  Memory speed is the bottleneck
  Prefetching scheme to overlap communication and computation
Improve previous work by optimizing memory use
  Use maximum DDR channels
  Improve compute vs bandwidth ratio with time skewing
    3.5K: time skewing
    through pipelining
  Leverage TURBOCARD2
  architecture,
- 6R

## Slide 17: Seismic processing on TURBOCARD2
x
y
dimX
dimX
R

## Slide 18: Seismic processing on TURBOCARD2
ISO-3DFD example
  Implemented on the MPPA using C compiler
  domain and velocity matrix, dimX = 152, R = 4
2.5D combined bandwidth
3.5K combined bandwidth, 2 timesteps
  Theorical ratio vs 2.5D: 30% less bandwidth needed
  Experimental results: 53% of performance increase
  5.6 Gcells/sec, which makes 0.07 Gcells/s/watt on Turbocard

## Slide 19: Conclusion on Seismic processing
Multi-level domain decomposition is cumbersome
Optimization is hard on many platforms despite having tools
  Halo sharing,
  Time skewing,
  Minimize datamovement, maximize the efficiency by reuse
Why doing it ever and ever again?
  Can we help people by providing a Seismic interface to offload stencil computation on our accelerator ?

## Slide 20: Kalray Seismic imaging on TURBOCARD2 Work-In-Progress
Seismic Imaging Processing Pipeline (workload scheduling, shots access, snapshots management…)
Seismic kernels
C/C++/Fortran
Seismic Imaging Processing Pipeline (workload scheduling, shots access, snapshots management…)
Kalray Seismic
Host API
Kalray Seismic Runtime
Pipeline setup,
Datamovers,
calling kernels
PCIe
x86
x86 + TURBOCARD
Seismic kernels
C/C++/Fortran
The seismic imaging processing pipeline is left untouched. Only the calls to the seismic kernels are modified to call Kalray Seismic Host API
Kalray will provide an easy API interface with the Seismic kernels
The seismic kernels are recompiled from the same source for TURBOCARD
Notes: Petits bouts de codes par rapport au reste, pas de filesystem,…
Idée: on prend les kernels sans retoucher le cœur des boucles
Multilevel domain decomposition
Host_API_Inputs (*kernels pointer, int rayon_stencil, matrice_3D domain, matrice_3D velocity, ….)
To extract the « kernels » from production
- Kalray sismic runtime : pipeline setup dynamically, synchro, kalray datamover,, steps management, call les kernels, synchro

## Slide 21: Thank you for your attention!
Yann Kalemkarian | yann.kalemkarian@kalrayinc.com
Benoît Ganne | benoit.ganne@kalrayinc.com
Chris Piercy | christopher.piercy@kalrayinc.com